PCI Express Single Port Fiber Optical Gigabit Ethernet Server/PC Adapter

Type Number:  S6200-GI210

Brand: Sinovo

Overview:

S6200-GI210 is the fourth Generation server adapter card ,this is Single-Port Gigabit Ethernet server adapter designed for entry-level servers and Audio-Video applications.

This adapter represents the next step in the Gigabit Ethernet (GbE) networking evolu- tion for the enterprise and data center offering Audio-Video-Bridging (AVB) sup- port, along with power management tech- nologies such as Energy Efficient Ethernet (EEE) and DMA Coalescing (DMAC).

Advanced Technologies of IntelI210 Chipset controller

Halogen free, storage over Ethernet, power management

Key Features

- Low-halogen1 single-port PCI-Express* 1000Mbps Ethernet adapter

- Innovative power management features including Energy Efficient Ethernet (EEE), DMA Coalescing, ultra-compact design, and a unique ventilated bracket for increased efficiency and reduced power consumption

- IEEE 802.1Qav Audio-Video-Bridging (AVB) for tightly controlled media stream syn- chronization, buffering, and reservation

- High-performing design supporting PCI Express* Gen 2.1 2.5GT/s

- Reliable and proven Gigabit Ethernet technology from Intel Corporation

- Audio-Video Bridging (AVB)

- Performance Optimization

- Power  Management  Technologies

- Energy Efficient Ethernet (EEE)

- Environmentally Friendly Design

- Stateless offloads and Performance Features

- Remote Boot Option

- Managebility

Technical Specification :

| Product Code | S6200-GI210 |
| --- | --- |
| Product Name | Server Network Card |
| Chipset | IntelI210 Gigabit Controller |
| Bus Interface | PCI Express* 2.1 (2.5GT/s) Support |
| Bus Width | X1 lane PCI Express operable in x1,x4,X8, x16 slots |
| Data rate supported per port | 1000Mbps/Port |
| Connectors | SFP Slot,(1000BASE-SX, 1000BASE-LX, 1000BASE-ZX). LC fiber optical cables. |
| Network interface type | Single-Port ,SFP*1,Fiber Optical Card,LC |
| Network standard | IEEE802.3auto-negotiation |
| Brackets | Half and full (two brackets) |
| Intelligent offloads | YES |
| Operating Temperature | 0℃~55℃ |
| Operating Humidity | 85% |
| Storage Temperature | -40℃~70℃ |
| Storage Humidity | 90% |
| Length | 10.3cm |
| Width | 6.8cm |
| Full-height end bracket | 12cm |
| Low-profile end bracket | 8cm |
| Packing Standard Size (Unit) | 23*14.6*2.7cm |
| OS Operation | Windows XP Professional x64 Edition SP2 Windows XP Professional SP3 Windows Vista SP2 Windows 7 SP1 Windows Server 2003 SP2 Windows Server 2008 SP2 Windows Server 2008 SP2 Core Windows Server 2008 SP2 (w/ Hyper-V role) Hyper-V Server 2008 SP2 (stand-alone version) Windows Server 2008 R2 SP1 Windows Server 2008 R2 SP1 Core Windows Server 2008 R2 SP1 (w/ Hyper-V role) Hyper-V Server 2008 R2 SP1 (stand-alone version) WinPE 1.6 (2003 PE) WinPE 2.1 (2008 PE) WinPE 3.0 (2008 R2 PE) Windows CE 6 (based on NDIS5.x) Windows CE 7/WEC7 (based on NDIS6.x) Windows Embedded Standard 7 Linux Stable Kernel version 2.6/3.x Linux RHEL 5.8 Linux RHEL 6.2 Linux SLES 10 SP4 Linux SLES 11 SP2 FreeBSD 9 DOS NDIS 1 DOS ODI EFI 1.1 UEFI 2.1 UEFI 2.3 VMware ESXi 5.02 VMware ESX M/N.next 3 (GA TBD) Xen 3 |

Advanced Software features

- Adapter fault tolerance (AFT)

- Switch fault tolerance (SFT)

- Adaptive load balancing (ALB)

- Teaming support

- IEEE 802.3ad (link aggregation control protocol)

- PCIe Hot Plug*/Active peripheral component interconnect (PCI)

- IEEE 802.1Q* VLANs

- IEEE 802.3 2005* flow control support

- Tx/Rx IP, TCP, & UDP checksum offloading (IPv4, IPv6) capabilities

- (Transmission control protocol (TCP), user datagram protocol (UDP),

- Internet protocol (IP)

- IEEE 802.1p*

- TCP segmentation/large send offload

- MSI-X supports Multiple Independent Queues

- Interrupt moderation

- IPv6 offloading — Checksum and seg

Using Environment

DELL Server,HP Server,IBM Server,INSPUR Server,Leno Server and other big server brand,

IT System Integrator,Cloud,Big Date Center,Workstation,PC,FTTD Solution(Fiber to the desk) for

Government,institution, School, personal using ,IDC etc.

Partners and End-Users

China Telecom, China Netcom, China Railcom, China Unicom, Space Unisign servers, Bank of China, Founder Technology, Dawning servers, Lenovo servers, IBM servers, HP servers, Dell servers, the Great Wall Broadband, Beijing Radio and Television General Institute, , World Chinese Youth Federation, Tsinghua Huambo, China Urban Planning and Design, Gehua, The People's Republic of China Ministry of Railways, China City Planning Information Network, etc.

Warranty

Sinovo Ethernet network cards and optical modules, a 3 months replacement and a 3 years global warranty.

Service&Support

Supply OEM,ODM Service,if need any help plz call this Tel: +86-0755-22676587

Emai to Sales@sinovocorp.com