PCI Express Dual Port Fiber Optical Gigabit Ethernet Server Adapter

Type Number: S6200-2G576

Brand: Sinovo

Overview

Sinovo S6200-2G576 is the second generation of product list.

Built with the Intel 82576 Gigabit Ethernet Controller, these new adapters showcase the next evolution in GbE networking features for the enterprise network and data center. These features include support for multi-core processors and optimization for server virtualization.

Advanced Technologies of Intel82576EB Chipset

Virtualization, intelligent offloads, storage over Ethernet

Key Features

- High-performing, 1000Mbps Ethernet connection

- Reliable and proven Gigabit Ethernet technology from Intel Corporation

- Scalable PCI Express* interface provides dedicated I/O bandwidth for I/O-intensive networking applications

- Optimized for virtualized environments

- Flexibility with iSCSI Boot and choice of dual- and quad-port adapters in both fiber and copper

- Designed for Multi-Core Processors

- Virtual Machine Device queues (VMDq)

- Intel® I/O Acceleration Technology

- Single-Root I/O Virtualization (SR-IOV)

- End-to-End Wired Security

- On-Board Management Features

Technical Specification :

| Product Code | S6200-2G576 |
| --- | --- |
| Product Name | Server Network Card |
| Chipset | Intel82576EB Gigabit Controller |
| Bus Interface | PCI Express*1.0a |
| Bus Width | X4 lane PCI Express operable in x4,X8, x16 slots |
| Data rate supported per port | 1000Mbps/Port |
| Optional Connection Parts | SFP Transceiver *2, (1000BASE-SX, 1000BASE-LX, 1000BASE-ZX). LC fiber optical cables. |
| Connectors | SFP Slot |
| Network interface type | Dual-Port ,SFP*2,Fiber Optical Card,LC |
| Network standard | IEEE802.3auto-negotiation |
| Brackets | Half and full (two brackets) |
| Operating Temperature | 0℃~55℃ |
| Operating Humidity | 85% |
| Storage Temperature | -40℃~70℃ |
| Storage Humidity | 90% |
| Length | 13.3cm |
| Width | 6.8cm |
| Full-height end bracket | 12cm |
| Low-profile end bracket | 8cm |
| Packing Standard Size (Unit) | 23*14.6*2.7cm |
| OS Operation | Windows Server 2012* Windows 8* Windows Server 2008 R2* SP1 Windows 7* SP1 Windows Server 2008* SP2 Windows Vista* SP2 Windows Server 2003 R2* Windows Server 2003* SP2 Linux* Stable Kernel version 3.x, 2.6,x Red Hat Enterprise Linux* 5, 6 SUSE Linux Enterprise Server* 10, 11 FreeBSD 9* |

Using Environment

DELL Server,HP Server,IBM Server,INSPUR Server,Leno Server and other big server brand,

IT System Integrator,Cloud,Big Date Center,Workstation,PC,FTTD Solution(Fiber to the desk) for

Government,institution, School, personal using ,IDC etc.

Partners and End-Users

China Telecom, China Netcom, China Railcom, China Unicom, Space Unisign servers, Bank of China, Founder Technology, Dawning servers, Lenovo servers, IBM servers, HP servers, Dell servers, the Great Wall Broadband, Beijing Radio and Television General Institute, , World Chinese Youth Federation, Tsinghua Huambo, China Urban Planning and Design, Gehua, The People's Republic of China Ministry of Railways, China City Planning Information Network, etc.

Warranty

Sinovo Ethernet network cards and optical modules, a 3 months replacement and a 3 years global warranty.

Service&Support

Supply OEM,ODM Service,if need any help plz call this Tel: +86-0755-22676587

Emai to Sales@sinovocorp.com