PCI Express 10G Dual Port Copper Server Adapter

Type Number：S6300-2TX540

Brand: Sinovo

Overview

Sinovo S6300-2TX540 10GBASE-T network adapter provides iSCSI，FCoE,Virtualization and

Flexible Port Partitioning.

Advanced Technologies

Virtualization, storage over Ethernet, FCoE, intelligent offloads

Key Features:

- Low Cost, Low Power, 10 Gigabit Ethernet (10GbE) Performance for the Entire Data center

- Standard CAT-6a Cabling with RJ45 Connectors

- Backward Compatibility with Existing 1000BASE-T Networks Simplifies the Transition to 10GbE

- Flexible I/O virtualization for port partitioning and quality of service (QoS) of up to 64 virtual ports

- Unified Networking Delivering LAN, iSCSI, and FCoE in One Low Cost CNA

- Industry First Dual-Port 10GBASE-T Adapter with Single-Chip Solution with Integrated MAC + PHY

- Reliable and proven 10 Gigabit Ethernet technology from Intel Corporation

Advanced Technologies of Intelx540 Chipset

Virtualization, storage over Ethernet, FCoE, intelligent offloads

10 Gigabit for the Broad Market

The Intel® Ethernet Converged Network Adapter X540 is the latest innovation in Intel’s leadership to drive 10 Gigabit

Ethernet into the broader server market. This adapter hosts Intel’s latest Ether- net silicon, the Intel® Ethernet Controller X540, which is used by many OEMs as a single chip solution for LAN on Mother-board (LOM) to deliver 10 Gigabit Ethernet (10 GbE) on the latest server platforms.

10GBASE-T Simplifies the Transition to 10 GbE

The Intel X540 family of products works with existing networks today. It works with legacy Gigabit Ethernet (GbE) switches and Cat 6A cabling. Install the Intel X540 adapter into a server and the auto-negotiation between 1 GbE and 10 GbE provides the necessary backwards compatibility that most customers require for a smooth transition and easy migration to 10 GbE. When time and budget allows, 10GBASE-T switches can be added any time to experience the full benefits of 10 GbE.

10GBASE-T uses the copper twisted pair cables that are very familiar to IT profes- sionals today. It is everything you know and love about 1000BASE-T. The knowl- edge, training and investment in BASE-T are preserved. 10GBASE-T is the easiest and most versatile 10 GbE and you can deploy it anywhere in your data center. Its flexible reach from 1 meter to 100 meters supports the latest network architectures including Top of Rack (ToR), Middle of Row (MoR), and End of Row (EoR).

10G Performance at Low Cost and Low Power

The new Intel® Ethernet Converged Network Adapter X540 is the lowest cost way to deploy 10 GbE in your data center today. The Intel X540 uses low cost, Cat

6 and Cat 6A cabling. Chances are this cabling already exists in the data center.

A way for Intel to reduce cost and power is to integrate components into a single- chip solution. Of course, integration is what Intel does best. With the new Intel X540 Controller, the MAC and the PHY are integrated into a single-chip solution.

So, why is integration important? First, integration translates to lower power. A single-chip solution simply uses less power than two separate components.

This means no more active heat sink and reduces the per-port power consumption. Second, integration also means lower cost per port. Manufacturing a single part costs less than two. When cabling is accounted for, cost efficiencies realized from a single part mean 10GBASE-T is the lowest cost media to deploy.

With lower cost and power, 10GBASE-T is ready for broad deployment. 10GBASE-T is an option for every rack and tower server in the data center. The wait for a low cost 10 GbE copper solution to broadly deploy 10 GbE to all corners of the data center

is over. The new Intel X540 adapter provides bandwidth-intensive applications with highly affordable 10 GbE network performance and cost-effective RJ-45 con- nectivity for distances up to 100 meters.

Technical Specification :

| Product Code | S6300-2TX540 |
| --- | --- |
| Product Name | Server Network Card |
| Chipset | Intel x540 10G Controller |
| Bus Interface | PCI Express* V2.1 (5 GT/s) Support |
| Bus Width | X8 lane PCI Express operable in x8, x16 slots |
| Bus Speed | 20Gbps uni-directional,40Gbps bi-directional |
| Date Rate support per port | 100Mbps,1Gbps,10Gbps |
| Network interface type | Dual-Port ,RJ45*2 Copper 10G |
| Network standard | IEEE802.3auto-negotiation |
| Brackets | Half and full (two brackets) |
| Cabling Distances | 10GBASE-T,100BASE-T,1000BASE-T |
| Intelligent offloads | YES |
| Operating Temperature | 0℃~55℃ |
| Operating Humidity | 85% |
| Storage Temperature | -40℃~70℃ |
| Storage Humidity | 90% |
| Length | 13.3cm |
| Width | 6.8cm |
| Full-height end bracket | 12cm |
| Low-profile end bracket | 8cm |
| Packing Standard Size (Unit) | 23*14.6*2.7cm |
| Storage Over Ethernet | Yes |
| Network operating Systems (NoS) Software Support | Windows* 7 (IA32 and X64) Windows Server* 2008 (x64 and IPF) Windows Server* 2008 Core (x64 and IPF) Windows Server* 2008 R2 (x64 and IPF) Windows Server 2008 R2 Core (x64 and IPF) Linux* SLES 11 SP1 Microsoft Windows Server 2003* Microsoft Vista* SUSE* SLES 10* or later, Professional 9.2 or later Microsoft Windows Virtual Server* 2005* Red Hat Enterprise* 4* or later FreeBSD* 5.x or later support VMware* ESX 4.0/4.1, ESXi 5.0 support Fedora* EFI* 1.1 |

S6300-2TX540 other  performances :

Exciting New data Center usage Models,Flexible i/o Virtualization ,Flexible Port Partitioning (FPP),unified Networking,iSCSi Simplifies SAN Connectivity ,open FCoE Consolidates LANs and Legacy SANs,data Center Bridging (dCB) delivers Lossless Ethernet

Using Environment

DELL Server,HP Server,IBM Server,INSPUR Server,Leno Server and other big server brand,

IT System Integrator,Cloud,Big Date Center,Workstation,PC,FTTD Solution(Fiber to the desk) for

Government,institution, School, personal using ,IDC etc.

Partners and End-Users

China Telecom, China Netcom, China Railcom, China Unicom, Space Unisign servers, Bank of China, Founder Technology, Dawning servers, Lenovo servers, IBM servers, HP servers, Dell servers, the Great Wall Broadband, Beijing Radio and Television General Institute, , World Chinese Youth Federation, Tsinghua Huambo, China Urban Planning and Design, Gehua, The People's Republic of China Ministry of Railways, China City Planning Information Network, etc.

Warranty

Sinovo Ethernet network cards and optical modules, a 3 months replacement and a 3 years global warranty.

Service&Support

Supply OEM,ODM Service,if need any help plz call this Tel: +86-0755-22676587

Emai to Sales@sinovocorp.com