PCI Express Single Port Fiber Optical 10G Ethernet Server Adapter

Type Number: S6300-S599

Brand: Sinovo

Overview:

The Sinovo S6300-S599 server adapter card with SFP+ connectivity, is the most flexible and scalable Ethernet adapters for today’s demanding data center environments. Data center networks are being pushed to their limits. The escalating deployments of servers with multi-core processors and demanding applications such as High Performance Computing (HPC), database clusters, and video-on-demand are driving the need for 10 Gbps connections. Customers require flexible and scalable I/O solutions to meet the rigorous requirements of running mission-critical applications in virtualized and unified storage  environments.

Advanced Technologies of Intel82599EN Chipset

Virtualization, storage over Ethernet, FCoE, intelligent offloads

Key Features

- Best Choice for Virtualization

- unified Networking and Storage :Support for fiber Channel over ethernet (fCoe),Support for iSCSi,

- Reliable performance:Security Optimizations,designed for Multi-core processors,pCie v2.0 (5 Gt/s)

- i/O features for Multi-core processor Servers

- Virtualization features

- Manageability features

Technical Specification :

| Product Code | S6300-S599 |
| --- | --- |
| Product Name | Server Network Card |
| Chipset | Intel8299EN Gigabit Controller |
| Bus Interface | PCI Express* V2.1 (5 GT/s) Support |
| Bus Width | X8 lane PCI Express operable in x8, x16 slots |
| SFP+ Connectivity | SFP+ connections support 10GBASE-SR, 10GBASE-LR and SFP+ Copper Direct Attach physical media. |
| Connectors | One or two LC fiber-optic connectors SFP+ Direct Attach cables |
| Network interface type | Single-Port ,SFP+*1,Fiber Optical Card,LC |
| Network standard | IEEE802.3auto-negotiation |
| Brackets | Half and full (two brackets) |
| Intelligent offloads | YES |
| Operating Temperature | 0℃~55℃ |
| Operating Humidity | 85% |
| Storage Temperature | -40℃~70℃ |
| Storage Humidity | 90% |
| Length | 13.3cm |
| Width | 6.8cm |
| Full-height end bracket | 12cm |
| Low-profile end bracket | 8cm |
| Packing Standard Size (Unit) | 23*14.6*2.7cm |
| Operating System | Windows 7 Windows Server 2008 R2 Windows Server 2008 R2 Core Linux SLES 11 SP1 Windows Vista* SP2 Windows Server* 2003 SP2 Windows Server 2008 SP2 Windows Server 2008 SP2 Core Linux* Stable Kernel version 2.6 Linux RHEL 4.8 Linux RHEL 5.5 Linux SLES 10 SP3 Linux SLES 11 FreeBSD* 8.0 EFI* 1.1 N/A N/A UEFI* 2.1 N/A |

Advanced Software features

- Adapter fault tolerance (AFT)

- Switch fault tolerance (SFT)

- Adaptive load balancing (ALB)

- Teaming support

- IEEE 802.3ad (link aggregation control protocol)

- PCIe Hot Plug*/Active peripheral component interconnect (PCI)

- IEEE 802.1Q* VLANs

- IEEE 802.3 2005* flow control support

- Tx/Rx IP, TCP, & UDP checksum offloading (IPv4, IPv6) capabilities

- (Transmission control protocol (TCP), user datagram protocol (UDP),

- Internet protocol (IP)

- IEEE 802.1p*

- TCP segmentation/large send offload

- MSI-X supports Multiple Independent Queues

- Interrupt moderation

- IPv6 offloading — Checksum and seg

Using Environment

DELL Server,HP Server,IBM Server,INSPUR Server,Leno Server and other big server brand,

IT System Integrator,Cloud,Big Date Center,Workstation,PC,FTTD Solution(Fiber to the desk) for

Government,institution, School, personal using ,IDC etc.

Partners and End-Users

China Telecom, China Netcom, China Railcom, China Unicom, Space Unisign servers, Bank of China, Founder Technology, Dawning servers, Lenovo servers, IBM servers, HP servers, Dell servers, the Great Wall Broadband, Beijing Radio and Television General Institute, , World Chinese Youth Federation, Tsinghua Huambo, China Urban Planning and Design, Gehua, The People's Republic of China Ministry of Railways, China City Planning Information Network, etc.

Warranty

Sinovo Ethernet network cards and optical modules, a 3 months replacement and a 3 years global warranty.

Service&Support

Supply OEM,ODM Service,if need any help plz call this Tel: +86-0755-22676587

Emai to Sales@sinovocorp.com